# LOCATING SEQUENTIAL STRINGS – Points

| CODE | PBOL |
| --- | --- |
| DESCRIPTION | Bollard |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PBPP |
| --- | --- |
| DESCRIPTION | Telephone |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |

| CODE | PBSS |
| --- | --- |
| DESCRIPTION | Bus Stop Sign |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PBXX |
| --- | --- |
| DESCRIPTION | Bore |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |

| CODE | PCAT |
| --- | --- |
| DESCRIPTION | Cathodic Protection Post |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PCBI |
| --- | --- |
| DESCRIPTION | Irrigation - Control Box |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Centre |
| COMMENTS |  |

| CODE | PCCB |
| --- | --- |
| DESCRIPTION | Cathodic Cables Box |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Centre |
| COMMENTS |  |

| CODE | PCMM |
| --- | --- |
| DESCRIPTION | Telecommunications Cable Marker |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PDHH |
| --- | --- |
| DESCRIPTION | Drill Hole |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Centre |
| COMMENTS |  |

| CODE | PECM |
| --- | --- |
| DESCRIPTION | ETSA Cable Marker |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Centre |
| COMMENTS |  |

| CODE | PEMP |
| --- | --- |
| DESCRIPTION | Environmental Marker Post |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS | Annotate with TSA number e.g. 720 |

| CODE | PFLL |
| --- | --- |
| DESCRIPTION | Floor Level |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Floor Level |
| COMMENTS |  |

| CODE | PFMP |
| --- | --- |
| DESCRIPTION | Fire Plug Marker Post |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |
| FIG 1.0 FIG 1.1 |

| CODE | PFMR |
| --- | --- |
| DESCRIPTION | Fire Plug Marker Reflector |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Centre |
| COMMENTS |  |
| FIG 1.0 FIG 1.1 |

| CODE | PGGG |
| --- | --- |
| DESCRIPTION | Grating |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Centre |
| COMMENTS |  |

| CODE | PGII |
| --- | --- |
| DESCRIPTION | Nail (GIN) |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at Centre of Head |
| COMMENTS |  |

| CODE | PGMP |
| --- | --- |
| DESCRIPTION | Gas Marker Post |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |
| FIG 1.0 FIG 1.1 |

| CODE | PHYY |
| --- | --- |
| DESCRIPTION | Hydrant |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PLBB |
| --- | --- |
| DESCRIPTION | Litter Bin |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |
| FIG 1.0 FIG 1.1 |

| CODE | PMBB |
| --- | --- |
| DESCRIPTION | Mail Box |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |

| CODE | PMGG |
| --- | --- |
| DESCRIPTION | Gas Meter |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |

| CODE | PMPB |
| --- | --- |
| DESCRIPTION | Pavement Bar |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at centre |
| COMMENTS |  |

| CODE | PMPP |
| --- | --- |
| DESCRIPTION | Metal Pin |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate on top of Pin |
| COMMENTS |  |

| CODE | PMWW |
| --- | --- |
| DESCRIPTION | Water Meter |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |
| FIG 1.0 FIG 1.1 |

| CODE | PMXX |
| --- | --- |
| DESCRIPTION | MARS Marker |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS | Annotate with distance e.g. 20 |

| CODE | PNSS |
| --- | --- |
| DESCRIPTION | Natural Surface - Point |
| MODEL | SURVEY MODEL |
| TINNABLE | YES |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION |  |
| COMMENTS | Spot height |

| CODE | PPBB |
| --- | --- |
| DESCRIPTION | Boundary Peg |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate on top of Peg |
| COMMENTS |  |

| CODE | PPEE |
| --- | --- |
| DESCRIPTION | Engineering Peg |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate on top of Peg |
| COMMENTS | Typically yellow |

| CODE | PPFF |
| --- | --- |
| DESCRIPTION | Fence Post |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |

| CODE | PPGG |
| --- | --- |
| DESCRIPTION | Guide Post |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PPSA |
| --- | --- |
| DESCRIPTION | Sign Post (one sided) |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PPSB |
| --- | --- |
| DESCRIPTION | Sign Post (two sided) |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |
| FIG 1.0 FIG 1.1 |

| CODE | PPTM |
| --- | --- |
| DESCRIPTION | Parking Ticket Machine |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |

| CODE | PPUU |
| --- | --- |
| DESCRIPTION | Petrol Pump |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS | Associated codes EC |

| CODE | PSBB |
| --- | --- |
| DESCRIPTION | Signal Box |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base/ centre for X/Y |
| COMMENTS |  |
| FIG 1.0 FIG 1.1 |

| CODE | PSKK |
| --- | --- |
| DESCRIPTION | Spike |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Survey on head |
| COMMENTS |  |

| CODE | PSPA |
| --- | --- |
| DESCRIPTION | Steel Pole |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS | Associated code PCAM |
| FIG 1.0 FIG 1.1 |

| CODE | PSSA |
| --- | --- |
| DESCRIPTION | Survey stations string |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION |  |
| COMMENTS |  |

| CODE | PSTA |
| --- | --- |
| DESCRIPTION | Stobie Pole |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PSUU |
| --- | --- |
| DESCRIPTION | Sump, Domestic |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at centre |
| COMMENTS |  |

| CODE | PTAA |
| --- | --- |
| DESCRIPTION | Tap |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PTPP |
| --- | --- |
| DESCRIPTION | Telecommunications Pillar |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PUPP |
| --- | --- |
| DESCRIPTION | Unknown Point |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION |  |
| COMMENTS | Annotate in model as *A text |

| CODE | PUPL |
| --- | --- |
| DESCRIPTION | Unknown Point (with level) |
| MODEL | SURVEY MODEL |
| TINNABLE | YES |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION |  |
| COMMENTS | Annotate in model as *A text |

| CODE | PVEE |
| --- | --- |
| DESCRIPTION | Sewer Vent |
| MODEL | SERVICES ASSET |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PWPA |
| --- | --- |
| DESCRIPTION | Wooden Pole |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |

| CODE | PWPS |
| --- | --- |
| DESCRIPTION | Wooden Pole and Sign |
| MODEL | SURVEY MODEL |
| TINNABLE | NO |
| DIRECTIONAL | N/A |
| LOCATION INFORMATION | Locate at base |
| COMMENTS |  |