Road & Marine Assets

ASSET TYPE AND CONDITION RATING EXAMPLES

– Roads Addendum

Document #: 12290952       Version 2.1

RAMA

# Table of Contents

1.	INTRODUCTION	5

1.1.	Purpose of this Document	5

2.	ASSET STATUS	5

2.1.	Operating Asset	5

2.2.	Renewing assets	5

2.3.	Decommioning or deleting assets	5

3.	ROAD ASSET TYPE EXAMPLES	6

3.1.	Sign posts	6

3.2.	Signs	7

3.3.	Safety Barrier	9

3.4.	Terminals	14

3.5.	Motorcycle Protection	21

3.6.	Drainage	23

3.7.	Inlet / Outlet / Junction	28

3.8.	Fence / Gates	32

3.9.	Stack Sites	34

3.10.	Retaining Wall	35

3.11.	Rest Area	37

3.12.	Bins	38

3.13.	Shelter	39

3.14.	Toilet Block	40

3.15.	Water Tank	40

3.16.	Median	41

3.17.	Pathways	44

3.18.	Bollards	45

3.19.	Windsocks	45

3.20.	Arrestor Bed	45

3.21.	Weigh Stations	46

3.22.	Park ‘N’ Ride	46

3.23.	Roadstrips	47

3.24.	Grids	47

3.25.	Floodway’s	48

4.	ASSET CONDITION EXAMPLES	50

4.1.	Sign posts	50

4.2.	Signs	53

4.3.	Safety Barrier	58

4.4.	Terminals	62

4.5.	Motorcycle Protection	64

4.6.	Drainage	66

4.7.	Inlet / Outlet / Junction	68

4.8.	Fence / Gates	70

4.9.	Stack Sites	71

4.10.	Retaining Wall	74

4.11.	Rest Area	75

4.12.	Bins	77

4.13.	Table	79

4.14.	Shelter	80

4.15.	Toilet Block	82

4.16.	Water Tank	83

4.17.	Median	85

4.18.	Pathways	88

4.19.	Bollards	89

4.20.	Windsocks	91

4.21.	Weigh Stations	93

4.22.	Grids	95

4.23.	Floodways	98

# DOCUMENT CONTROL

## DOCUMENT HISTORY

| Document Name | Version | Release Date |
| --- | --- | --- |
| RAMA-AM-PRC-005 - Roads Addendum | Rev 1 | 1 August 2018 |
| RAMA-AM-PRC-005 - Roads Addendum | Rev 2 | July 2019 |
| RAMA-AM-PRC-005 - Roads Addendum | Rev 2.1 | Dec 2019 |

- INTRODUCTION

Purpose of this Document

The purpose of this document is to clarify the variety of road asset types and provide a guidance for selecting the asset condition rating as described within Road and Marine Asset Data Collection Manual (RAMA-AM-PRC-005).

- ASSET STATUS

Operating Asset

Operating status shall be used for all assets that are currently in operation.

Renewing assets

When an asset is renewed the asset condition rating changes to “new” and the installation date is to be updated. For features such as signs the manufacture date is also required.

Decommioning or deleting assets

Where a road asset has been removed or decommissioned, the asset status should change from “Operating” to “Decommissioned”. The decommissioning date shall be entered into the field comment.

When an asset is removed completely, the asset status changes from “Operating” to “Deleted”. The date of removal shall be entered into the field comment.

- ROAD ASSET TYPE EXAMPLES

Sign posts

Types

| Aluminium Frangible | Steel I Beam Slip Base Posts |
| --- | --- |

| Steel Flex | Poly-flex |
| --- | --- |

Frangible

All 80x40 posts are frangible.

Circular posts may not be considered frangible depending on the speed environment. Refer to table below for assistance (Master Specification R49).

Signs

Types

Refer to DPTI ‘s Standard Road Sign Index Link for sign type information:

http://www.dteiapps.com.au/signindx/Search.aspx

Regulatory RX - R Series

Warning RX – W Series

Guide GX – G3 series, G6 Series, G7 (Standard), G9 (Standard), G10 Series, GE6 Series,

Hazard DX – D Series

Note: Against the sign type the size code (i.e. A, B, C, D) shall be added for all signs.

A TES number shall be included for the following signs:

Tourist – G8 Series (non Standard), G11 Series, GE11 Series (TOUR)

Service – G7 Series (non Standard) GE7 Series (SERV)

Information –G4 Series, GE4 Series (REAS), G9 (non standard), Information (INFO),

Road Safety (RSS)

Direction – G1 Series (AD/ASN), G2 Series (ID), GE1 Series (AD/ASN), GE2 Series (ID)

Maintenance Marker (TES 13824)

Other – Warning (WARN), Regulatory (REG), Misc (MISC),

Road Side Significant Sites (TES 12564), Bikeway (BKWY), Tunnel (TUNL)

Note: Sign code for TES signs use information given in the G series or brackets above.

Refer to DPTI Sign Map Server for to obtain the TES number and sign information:

http://itims.dpti.sa.gov.au/Asset/Signs/

| MAINTENANCE MARKERS (TES 13824) | ROAD SIDE SIGNIFICANT SITES (TES 12564) |
| --- | --- |

Dynamic Type

| Static | CMS – Changeable Message Sign |
| --- | --- |

| VMS – Variable Message Sign | Static & Lights |
| --- | --- |

Safety Barrier

Barrier Types

Backing Rail

Bridge Rail

TBC

Concrete Barrier

Thrie Beam

Wire Rope Briffin

Wire Rope Sentryline

Wire Rope Flexfence

| Ezy-Guard Smart | W Beam |
| --- | --- |
| “Z” shaped posts, no spacer |  |

| Armorguard | BarrierGuard Gate |
| --- | --- |

Masonry Wall

Aluminium RHS

Steel RHS

Steel Panel

Steel Pipe

Sentry W-Beam

“C” shaped posts, no spacer. Smaller that traditional W beam posts.

Ezy-Guard High Containment

“Z” shaped posts & no spacer

Terminals

Type

| MELT – Modified Eccentric Loader Terminal |
| --- |
| Melt (Older Assembly) | Melt (Current Assembly) |
| Melts Terminal Length are 12m long. Trailing Melt terminals (End) of 4m in length maybe used where there is no possible impact from opposite direction. |
| Trailing Melt terminal |

BCT – Breakaway Cable Terminals

Typically made with wooden posts with plate at the front and the first 2 post having holes.

BCT Start Terminal Length is 8m long, however there are some that are 4m long. For 8m lengths first 2 posts are wooden, group of posts closer together or not bolted to the post (like Melts), followed by 2 posts of standard distance apart. For 4m lengths first 2 posts are wooden then 2 posts of standard distance apart. Trailing BCT terminals (End) are generally 4m long.

SKT – Sequential Kinking Terminal

SKT (Supplied by Safer Direction) are a square head. Installation is generally straight, but can flared by a maximum of 600m from rest of the barrier.

Terminal Lengths are 8m or 16m End of the terminal is at the location which the black spacer blocks finish

FLEAT – Flared Energy Absorbing Terminal

FLEAT (Supplied by Safer Direction) have a rectangular head. Generally flared installation.

Terminal Lengths are 8m or 12m End of the terminal is at the location which the black spacer blocks finish

ET-2000 Plus – Extruder Terminal

ET-2000 Plus (Supplied by Ingal) has Rectangular head. Key difference between an ET-2000 and FLEAT is the strut installed in between the first and second post.

Terminal Lengths are 8m or 16m 8m lengths are only to be used in speed environments of less than 70km/h. 16m length can be used at any speed. End of the terminal is at the location which the black spacer blocks finish

TREND 350

TREND 350 (Supplied by Ingal) is a Rectangular noise. Key difference between a TREND 350 and ET 2000 is continual cut openings along the length of the W section of the terminal. There is no cage to guide the head along the W beam.

Terminal Lengths are only 12m long. Can only be used in speeds less than 100km/h

X-Tension

X-Tension (Supplied by ACP) is easily identified with the large yellow head.

Terminal Lengths are only 12m long.

Fishtail Terminal

Fishtail terminals are 0.75m length. Should only be use where there isn’t any possibility of spearing if impacted by vehicles.

Omni Stop End

Omni Stop End (Supplied by Safer roads) may get confused by a Melt with the end barrel; however the key difference is the circular end post vs the traditional C section posts.

Terminal Lengths are only 2.5m long. Can only be used in speeds less than 70km/h

Driveway

Driveway terminals are constructed the same way as Melts or BCT, however the terminal turns 90 degrees compared with the slight flaring of the terminal. Used for opening into driveways or roads.

| QuadGuard | Smart Cushion |
| --- | --- |
| Single sliding mechanism in the Centre | Square shaped no barrels along |

| Universal TAU-II | TRACC |
| --- | --- |
| Thrie Beam along the side | Dual sliding Mechanism on the sides. |

| EAPTB Stobie Buffer | Treefend |
| --- | --- |

RAPTOR

Motorcycle Protection

Types

Stack Cushion

MPR

MPR can be identified with the ridge at the top and bottom.

HIASA SPM-ES2

HIASA SPM-ES2 can be identified with the ridge only at the bottom.

Drainage

Types

Pipe Culvert

Box Culvert

Subsoil Drain

Grate

Lined Drain

Swale

Bioretension Swale

Arch

Wetland

Sedimentation Basin

Detention Basin

Inlet / Outlet / Junction

Types

Headwall

SEP

Grate

SEP / Grate Combo

Field Gully

Junction Box

HUMEceptor

Stormceptor

Downstream Defender

EcoSol RSF 4000

Gross Pollution Trap

TBC

Trash Nets

Fence / Gates

Types

Farm or Stock

| Chainmesh | Pedestrian |
| --- | --- |

| Vermin Proof | Concrete Panel |
| --- | --- |

| Timber Panel | Security fence |
| --- | --- |

| 1200 Pedestrian Rail and 600 Pedestrian Rail | Stock Gate |
| --- | --- |

| Pedestrian Gate | Security Gate |
| --- | --- |
|  | TBC |

| Motorised Security Gate | Other eg |
| --- | --- |
| TBC |  |
|  | Other include Koala Crossing in comments add “Koala Crossing” |

Stack Sites

Retaining Wall

Types

| Concrete Block | Concrete Crib |
| --- | --- |

| Timber Crib | Gabion |
| --- | --- |

| Shotcrete | Stone Walling |
| --- | --- |

| Reinforced Concrete | Reinforced Earth – Concrete Faced |
| --- | --- |

| Reinforced Earth - Concrete Panel | Reinforced Earth – Gabion Faced |
| --- | --- |

| Reinforced Earth - Keystone | Stone Pitched |
| --- | --- |

Steel Post & Concrete Panel

Rest Area

Refer to Operational Instruction 20.3 to determine if a rest area is Major, Minor or Truck Parking Truck Parking informal.

Truck Parking – Unless the rest area is signed with No Trucks Parking Symbol (S23) truck parking is recorded as “Y”

Bins

| Plastic | Concrete |
| --- | --- |

| Metal | Other |
| --- | --- |
|  | TBC |

Table

| Metal | Wood |
| --- | --- |

| Recycled Plastic | Other |
| --- | --- |

Shelter

| Cantilever | Truss |
| --- | --- |

| Sails | Other |
| --- | --- |
|  | TBC |

Toilet Block

Water Tank

Median

Types

| Kerbed Median | Barrier |
| --- | --- |
|  | Median concrete barrier should also be recorded under Safety Barriers “Concrete”. |

No Edge

Median Infill

Infill type is for the majority of the median, unless Deciduous Trees.

| Paved | Concrete |
| --- | --- |

| Asphalt | Synthetic Turf |
| --- | --- |

| Rubble | Grassed |
| --- | --- |

| Deciduous Trees | Mulched |
| --- | --- |

| Rock Filled | Other Landscaping |
| --- | --- |
|  | TBC |
|  | If a median has multiple types (e.g. Grassed and trees) record as “Other Landscaping” and note what there is in the comments |

Pathways

| Pedestrian | Shared Use |
| --- | --- |
| No signage footpaths | Signed with R8-2 |

| Bicycle | Other |
| --- | --- |
|  | TBC |
| Signed with R8-1 and/or R6-10-3 |  |

Bollards

| Timber | Steel Removable |
| --- | --- |

Windsocks

Arrestor Bed

Weigh Stations

Park ‘N’ Ride

Roadstrips

Grids

Types

| DPTI Design and construct | Aprilla |
| --- | --- |

Gridrite

Floodway’s

| Unsealed | Stabilised |
| --- | --- |

| Sealed | Concrete |
| --- | --- |

- ASSET CONDITION EXAMPLES`

Asset Condition rating within the Road and Marine Assets Data Collection Manual is provided in the Table below. Images within this section are used as a guide to assist in defining the various condition ratings.

| 1 | New | As new |
| --- | --- | --- |
| 2 | Good | No corrosion or other deterioration |
| 3 | Average | Some deterioration but structural integrity satisfactory. (eg. some corrosion of steel but strength not affected) |
| 4 | Poor | Considerable deterioration so that structural integrity compromised. (eg. steel corroded to extent that strength may be affected, cracked concrete posts) |
| 5 | Unserviceable | Deteriorated to extent that structural integrity is severely affected. (eg. severely corroded rail, spalled concrete posts, deteriorated timber components) |

Sign posts

New

Good

Average

Poor

Unserviceable

Signs

New (No signs of damaged or fading)

Night (Reflectivity 100-90%)

TBC

Good (Full sign visible, minor damages or fading)

Night (Reflectivity 90-75%)

TBC

Average (Majority of the sign is still visible, 30-50% damaged or fading)

Night (Reflectivity 75-65%)

TBC

Poor (Sign’s message has been impacted by damages / fading)

Night (Reflectivity 65-50%)

TBC

Unserviceable (Sign cannot be seen clearly, majority of reflective material peeling / cracked)

Night (Reflectivity 50-0%)

TBC

Safety Barrier

New (Installed in the last 10 years)

Good (Installed in the last 10-20 years)

Average (Installed in the last 20-30 years)

Poor (Installed in the last 30-40 years)

Unserviceable (Installed in 40+ years)

Terminals

Steel condition components refer to barriers for examples.

New (Installed in the last 10 years)

Good (Installed in the last 10-20 years)

Average (Installed in the last 20-30 years)

Poor (Installed in the last 30-40 years)

Unserviceable (Installed in 40+ years)

Motorcycle Protection

As motorcycle protection have only been installed for the last 15 years, it is not expected to have any poor or unserviceable motorcycle protection. Steel condition components refer to barriers for examples.

New

TBC

Good

Average

TBC

Poor

TBC

Unserviceable

TBC

Drainage

New

Good

Average

Poor

Unserviceable

Inlet / Outlet / Junction

Condition examples to be provided at later date

New

TBC

Good

Average

TBC

Poor

Unserviceable

TBC

Fence / Gates

New

Good

Average

Poor

Unserviceable

Stack Sites

New

TBC

Good

Average

Poor

Unserviceable

Retaining Wall

New

Good

Average

Poor

Unserviceable

TBC

Rest Area

Condition based on surface condition. Increasing amount of cracking, bleeding or pot holing within the rest are will determine the condition.

New

TBC

Good

Average

TBC

Poor

TBC

Unserviceable

TBC

Bins

New

Good

Average

Poor

Unserviceable

Table

Additional images on condition will be provided on next version. Refer to retaining walls for concrete table examples of cracking. Bins for plastic and metal condition ratings.

New

TBC

Good

Average

TBC

Poor

TBC

Unserviceable

TBC

Shelter

New

Good

Average

Poor

TBC

Unserviceable

TBC

Toilet Block

New

Good

Average

Poor

TBC

Unserviceable

Water Tank

New

Good

Average

Poor

TBC

Unserviceable

Median

Condition is based on the concrete kerbing and not the infill.

New

Good

Average

Poor

Unserviceable

Pathways

Refer to median for general condition ratings of concrete pathways.

New

Good

Average

Poor

Unserviceable

Bollards

New

Good

Average

TBC

Poor

Unserviceable

Windsocks

New

Good

Average

TBC

Poor

Unserviceable

Weigh Stations

New

TBC

Good

Average

Poor

TBC

Unserviceable

TBC

Grids

New

Steels in good condition No material build up, no spalling

Good

Steels in good condition Minimal Soil

Average

Spalling on abutments Grid half full of soil Rusting Broken weld

Poor

Spalling on abutments Grid full of soil Rusting Rusting

Unserviceable

Spalling on abutments Grid full of soil and in unrepairable condition

Floodways

New

Good

Average

Poor

Unserviceable

# Text boxes

RAMA-AM-PRC-005