|  | Transport Services Division |
| --- | --- |
|  | GEOSPATIAL SERVICES |
|  | Standards & Operational Procedures |

| Engineering Contractor Compliance Checklist SUR-CT003-1 |
| --- |
| To be completed by Contractor and forwarded to DPTI Contract Manager with each project |
| Contractor: |  | Job No: |  |
| Project Description (Road Name): |  |

| Clause | Heading or Description of Clause | Compliance | Details of Non-Compliance (Attach separate statement if insufficient space) | Auditor Only |
| --- | --- | --- | --- | --- |
| Contract Specification | Survey satisfies defined corridor and requirements |  |  |  |
| Tender 2011-050 Documents | Party Leader Qualifications |  |  |  |
| 2 | Survey Control (Horizontal & Vertical) |  |  |  |
| 3 | Survey Control accuracy (Horizontal & Vertical) |  |  |  |
| 3 Independent checks (QQ Model) |  | Urban | Rural |  |  |  |
|  | Hard Stand Features | 20mm Horizontal | 30mm Horizontal |  |  |  |
|  |  | 20mm Vertical | 30mm Vertical |  |  |  |
|  | Non Hard Stand Features | 100mm Horizontal | 150mm Horizontal |  |  |  |
|  |  | 50mm Vertical | 100mm Vertical |  |  |  |
| 4.1 | String Location requirements |  |  |  |
| 4.2 | Models provided meet project requirements |  |  |  |
| 4.2.3 | Survey DTM verified |  |  |  |
| 4.3 | Annotation |  |  |  |
| 5.11 (b) | Additional vegetation requirements (if required) |  |  |  |
| Items to be supplied by Contractor 4.4 | Project Report, U/G marked to DBYD plans, pdf file showing photographs of signs |  |  |  |
| Engineering Survey Guidelines (Optional) |
| 3 (Guidelines) | CHE checks recorded to two adjacent stations |  |  |  |
| 4 (Guidelines) | QQ checks recorded minimum of one per station setup |  |  |  |
|  |  | Urban | Rural |  |  |  |
| 5 (Guideline) Tolerances | CHE checks | <=7mm/100m | <=10mm/100m |  |  |  |
|  | CHE checks <=100m | <=7mm | <=10mm |  |  |  |
|  |  | Urban | Rural |  |  |  |
|  | Distance between shots | <=10 metres | <=15 metres |  |  |  |