First Published: December 2000

7th Version: March 2017

This document has been prepared by the Stormwater, Environment and Heritage unit in the Safety and Service Division. It has been approved and authorised for use by Departmental staff and its authorised agents by:

Director, Projects

Cover photographs: Native plants killed by Phytophthora on Kangaroo Island (courtesy Department of Environment and Natural Resources)

Extracts may be reproduced providing the subject is kept in context and the source is acknowledged. Every effort has been made to supply complete and accurate information. This document is subject to continual revision and may change. To ensure you have the most up to date version of this document refer to

Home - Department for Infrastructure and Transport - South Australia (dit.sa.gov.au)

For information regarding the interpretation of this document please contact:

Stormwater, Environment and Heritage Unit, Technical Services, Asset Management

Telephone: (08) 8343 2398

Phytophthora (Dieback) Control Environmental Instruction 21.3

CONTENTS

1.	Introduction	4

2.	Scope	4

3.	Phytophthora control principles	5

4.	Known infestations and areas potentially under threat of Phytophthora	6

4.1	High Potential Threat Areas	11

4.2	Moderate Potential Threat Areas	11

4.3	Low Potential Threat Areas	12

5.	Phytophthora risk assessment	12

6.	Phytophthora Hygiene Procedures	14

6.1	High Risk Sites	14

6.2	Medium Risk Sites	19

6.3	Low Risk Sites	20

7.	References	21

APPENDIX 1. 	DPTI roads within Phytophthora High Potential Threat Areas	22

APPENDIX 2. 	Hygiene guidelines for vehicles	23

APPENDIX 3:	Phytophthora Hygiene Procedure for Minor Works and Site Inspections	27

APPENDIX 4.	Phytophthora Hygiene Kit	29

APPENDIX 5. 	Native plant species susceptible to Phytophthora	32

# Introduction

Phytophthora is a parasitic pathogen that lives in soil and water and attacks the roots and basal stems of plants. This pathogen has been introduced to South Australia and can cause extensive damage to native vegetation by killing or injuring native plants. There are seven species of Phytophthora known to affect native vegetation. Phytophthora cinnamomi is the species most frequently associated with dying vegetation affected by Phytophthora. The only outward sign of its presence is sickness or death of the plants it attacks.

Phytophthora is a significant threat to native flora. In South Australia dieback caused by Phytophthora has been found in a number of sites within high rainfall areas, in particular the Adelaide Hills, Fleurieu Peninsula and Kangaroo Island. Phytophthora also affects many agricultural plant species.

New infections of Phytophthora are mainly caused through human activities involving the movement of infested soil and roots, and by water. Consequently, the only way to prevent Phytophthora from spreading is by controlling these human activities. High-risk areas for Phytophthora include high rainfall areas of the state with remnant native vegetation (see Figures 1 to 4). In transport corridors, high risk activities include working in native vegetation in wet areas and low lying areas such as road verges, drains, watercourses and wetlands, and sites adjacent to significant remnant native vegetation in close proximity to known infestations.

A wide range of activities undertaken within or associated with the maintenance of transport corridors, can spread Phytophthora. These include shoulder grading, drain clearing, earthmoving, stock-piling, vegetation control, extraction of raw materials, off-road vehicle use, site inspections and survey works. Other activities such as firebreak construction and maintenance, fencing, drilling, land clearing and the installation of services such as power, gas, telecommunications and water can also spread the pathogen.

There is no known method to eradicate Phytophthora once it has become established. Therefore appropriate hygiene procedures as identified in Section 6 must be adopted to minimise the risk of spreading Phytophthora.

# Scope

The Department of Planning, Transport and Infrastructure (DPTI) has a responsibility to ensure that its activities, and the activities of its contractors, do not adversely impact on the environment. This includes ensuring that Phytophthora is not introduced or spread by its activities, and those of its contractors.

The risk of spread of Phytophthora can be minimised by the adoption of appropriate management procedures within the control zones, as outlined in this Environmental Instruction. Like all quarantine procedures they can be made ineffective by even a single failure.

The goal of this Environmental Instruction is to protect remnant vegetation by minimising the risk of introducing and spreading Phytophthora.

This Instruction applies to all activities undertaken by DPTI, contractors to DPTI and their subcontractors, or lessees of property under the responsibility of DPTI, including:

- routine maintenance;

- construction;

- field inspection and survey; and

- landscaping and land management works.

# Phytophthora control principles

In general, the risk of spreading Phytophthora can be minimised by keeping machinery, equipment and footwear clean from soil or plant material, and by not further dispersing soil or plant material within a site. Movement of soil, plant material and water can spread Phytophthora and therefore must be controlled. Collectively these controls are called Phytophthora hygiene procedures.

The following principles apply to reducing the risk of spreading Phytophthora, particularly within High Risk Areas:

Avoid leaving formed areas

Avoid contact with the natural soil. Restrict movement of vehicles and personnel to the road formation, and other formed areas such as stockpile sites and borrow pits, particularly in wet conditions.

Avoid work in wet conditions

Operations should be carried out under dry soil conditions, particularly during the higher risk months of August to November inclusive. This is particularly important for high-risk activities such as drain cleaning and grading.

Ensure equipment is clean

Phytophthora is spread in soil or water. Objects (boots, vehicles, plant or equipment) must be free of soil, mud, slurry consisting of soil and water, or plant material especially roots and lower stems. All machinery must be clean before leaving the depot for a new work site, and before leaving the work site.

When in the field, all plant and equipment should be cleaned or washed down when moving:

- from Phytophthora-infested to Phytophthora-free or Phytophthora-status unknown areas, and

from Phytophthora-status unknown to Phytophthora-free areas.

Avoid native vegetation

Select plant lay-down areas or stockpile sites away from native vegetation and watercourses. Select sites down-slope of native vegetation.

Avoid sites prone to flooding or ponding

These are sites at high risk of infection. Work within drains and watercourses is a high-risk activity.

Ensure raw materials are Phytophthora-free

Raw materials must be sourced from Phytophthora-free pits. These areas must be secured against unauthorised entry.

Use low impact vegetation control methods

Vegetation control methods that do not disturb the soil such as mowing, slashing or herbicide application should be used in preference to grading.

# Known infestations and areas potentially under threat of Phytophthora

Areas of the State that are vulnerable to Phytophthora (i.e. where rainfall and temperature are conducive to disease) are shown in Figures 1 and 2. Figures 3 and 4 show known (reported) infestations.

High Potential Threat Areas are those parts of the State that occur above the 500mm rainfall isohyet (including the eastern portion of Kangaroo Island receiving less than 500mm annually) and may contain soils that are conducive to the establishment of Phytophthora.

Moderate Potential Threat Areas of the State occur between the 400mm and 500mm rainfall isohyets, with the exception of eastern Kangaroo Island.

Low potential threat areas are the remainder of the state.

The need for further assessment of risk, and application of control procedures, is dependent on whether the work or activity is proposed to be undertaken in a High, or Moderate Potential Threat Area of the State. No further assessment of risk is required for work proposed to be undertaken within the Low Potential Threat Area.

The outcome of a risk assessment for a particular site is whether the site is a High, Medium or Low Risk with regard to the need to implement appropriate Phytophthora hygiene procedures. The risk assessment process is described in Section 5 below.

Figure 3

Figure 4

## High Potential Threat Areas

Definition

High Potential Threat Areas of the State are those which are conducive to the spread of Phytophthora and the establishment of disease, based on climatic and soil factors and location of known infestations (Figures 1 to 4 and Appendix 1). Phytophthora is known to be present at sites within these areas.

The High Potential Threat Areas are:

- Mt Lofty Ranges (Angaston to Cape Jervis)

- Kangaroo Island.

Procedure

Within High Potential Threat Areas, Phytophthora control procedures may not be necessary at every site where an activity or work is to occur. Each work site must be assessed to determine if it is High, Medium or Low Risk (Section 5). Relevant information may be provided in a Vegetation Assessment or Vegetation Survey. An individual project may have multiple sites, including a material source (e.g. quarry), each of which must be classified according to risk.

## Moderate Potential Threat Areas

Definition

Moderate Potential Threat Areas of the State occur where Phytophthora has not yet been recorded but where there is a moderate potential of it becoming established (Figures 1 and 2).

The Moderate Potential Threat Areas are:

- Parts of the Adelaide Plains and Mid-North

- Southern Eyre Peninsula

- South East

- Southern Yorke Peninsula.

Procedure

Within Moderate Potential Threat Areas, Phytophthora control procedures may be necessary if a proposed work site has been assessed as a High or Medium Risk (Section 5). An individual project may have multiple sites, including a material source (e.g. quarry), each of which must be classified according to risk.

Within Moderate Potential Threat Areas of the State, High or Medium Risk sites have a greater potential to occur where:

- native vegetation containing susceptible species in or adjacent to the site is present,

- the site is located between 5 km and 10 km from a known infested site (irrespective of whether susceptible species have been identified in or adjacent to the site), and

- the land is prone to flooding or ponding.

## Low Potential Threat Areas

Definition

Low Potential Threat Areas of the State exist where Phytophthora has not yet been recorded and where there is a low likelihood of it becoming established.

Low Potential Threat Areas include parts of the State that are neither High Potential nor Moderate Potential Threat Areas (Figures 1 and 2).

Procedure

No Phytophthora control procedures are required in Low Potential Threat Areas.

# Phytophthora risk assessment

Within High Potential and Moderate Potential Threat Areas of the State, each site must be assessed prior to commencement of works onsite to determine if there is a High, Medium or Low risk of Phytophthora becoming established or spreading. Unless otherwise specified, this risk assessment must be undertaken by the Contractor.

The risk assessment must analyse the likelihood and consequence of infection for species of flora and ecological communities at the site. Once the assessment is completed, the level of risk and the Phytophthora control procedures appropriate to the site risk must be recorded in the Contractor’s Environmental Management Plan. These Phytophthora control procedures must then be implemented.

The key steps in the process of risk assessment to determine the appropriate level of Phytophthora control procedures are outlined in Figure 5.

Figure 5. Risk assessment process

1 Susceptible species include remnant native vegetation (see Appendix 4 for full list of susceptible species)

2 Conducive soil types: acidic soils with a low pH (<4). If the soil is alkaline with a high pH (>7) the soil is not considered a conducive soil type (i.e. limestone).

# Phytophthora Hygiene Procedures

## High Risk Sites

High Risk Sites may occur within the High Potential Area or Moderate Potential Area of the State only. Within the Moderate Potential Area, a High Risk Site would typically occur in a low lying area with relatively high soil moisture levels, adjacent to a significant remnant of native vegetation, with a confirmed infestation within 5 km of the site (irrespective of whether susceptible species have been identified in or adjacent to the site).

Definition

- Site is within a Medium or High Potential Threat area;

AND

- Site occurs within or adjacent to significant remnant native vegetation;

AND

- Conducive soil types are present;

AND

- The site meets any of the following criteria:

- it is located within 5 km of a confirmed infested site - irrespective of whether susceptible species have been identified in or adjacent to the site (NatureMaps

- NatureMaps Home (environment.sa.gov.au

- it is confirmed or suspected to be infested; and/or

- disease symptoms are present.

Pre-Works and On-Site Management Measures

The following procedures apply to any work site that has been designated as a High Risk Site. As the focus is on prevention of disease establishment or spread, High Risk Sites must be avoided wherever practicable (including material sources). The Contractor must implement the following management measures where a High Risk Site cannot be avoided.

Guidelines are given in Appendix 2 and Appendix 3 for the cleaning and wash-down of vehicles, equipment and footwear, where this has been identified in the following procedures.

Hygiene Plan

The Contractor must:

- prepare a Phytophthora Hygiene Plan in advance of works. This plan may form part of a Contractor’s Environmental Management Plan (CEMP);

- identify the location of any disease boundaries (e.g. known sites containing and adjacent to Phytophthora infestations);

- identify the necessary control measures, including no go zones where appropriate,

- indicate equipment access and soil handling activities;

- indicate the work site access and materials sources; and

- nominate the location and construction method of wash down areas (in accordance with the management measures outlined in Appendix 2).

Training

The Contractor must include relevant information and procedures to minimise the risk of spreading Phytophthora in the pre-works induction for all personnel working on the site.

In addition, the startup or toolbox meetings must include relevant information and procedures to minimise the risk of spreading Phytophthora.

Vehicle movement

The Contractor must contain movement of vehicles to formed areas wherever practicable, particularly in wet conditions.

The Contractor must ensure all plant is cleaned with Phytoclean® or sodium hypochlorite (pool chlorine) prior to:

- arriving at a site;

- moving to another High or Medium Risk site; and

- transporting gravel and other construction materials.

The Contractor must ensure plant is washed down in designated wash down areas.

The Contractor must ensure that work proceeds from un-infested (Phytophthora-free) or status unknown sites to known infested sites, wherever practicable.

Photo Credit: Alcoa, Dieback Management, http://www.alcoa.com/australia/en/info_page/mining_dmanagement.asp, accessed July 2015.

Earthworks

Wherever practicable, the Contractor must:

- avoid leaving the road except under dry soil conditions;

- avoid using tracked vehicles as they are difficult to clean effectively;

- avoid grading beyond the areas previously graded (e.g. patrol grading); and

- conduct routine activities in “bounds” of several kilometres (e.g. 3-4 km), each interrupted by a clean-down to minimise the exposure risk of vegetation down-slope of the operation.

Topsoil removal

The Contractor must contain topsoil within the infested area or dispose of it to a licensed waste depot where applicable.

If offsite disposal is required, the Contractor must secure and contain the material for transport, to prevent any potential to spread Phytophthora.

Drains

Wherever practicable, the Contractor must:

- clean out or repair drains in dry conditions only, unless during an emergency;

- avoid grading in watercourses or areas prone to flooding;

- ensure drains are constructed to avoid ponding of discharge water; and

- clean or wash down plant and equipment before moving away from a culvert or drain, if working outside formed areas.

Vegetation management and disposal

The Contractor must use vegetation control methods that do not disturb the soil, such as mowing, slashing, hand-pruning or herbicide application, in preference to grading.

Wherever practicable, the Contractor must carry out all works outside the formation in dry conditions only. The Contractor must avoid drains wherever practicable.

Where practicable, the Contractor must clearly mark on site, e.g. via bunting and signage, the areas which have been identified as Phytophthora-infested.

The Contractor must dispose of vegetation in the following way:

- Trees for removal must be cut a minimum of 1 metre above the ground. The vegetative material above this point (upper trunk and canopy) can be considered Phytophthora free as long as it has not been in contact with soil, and must be mulched and retained on site, or must be disposed of at the discretion of the Contractor, subject to Contract requirements.

- Vegetative material from weed species cut a minimum of 1 metre above the ground must be disposed of in accordance with Master Specification Part CH50 Environmental Protection Issues and any relevant Contract Specific Requirements.

- All vegetation under 1 metre, including tree stumps, must be excavated, stockpiled at a nearby secure location (to prevent unauthorised collection for firewood) and burnt once dry, if practicable. The material must be burnt on site or at a suitable location proposed by the Contractor and approved by the Principal. The Contractor must comply with all fire bans and restrictions, and must obtain an appropriate permit from the Local Council Authorised Officer or other relevant authority, and approval from the landowner, to carry out burning.

Alternatively, the stumps can be ground out in accordance with Master Specification Part L40 Tree Pruning and Removal and any relevant Contract Specific Requirements. Where there is ground vegetative material that is not from a weed species, it is to be retained and spread on site.

- All other vegetation (native and exotic) under 1 metre in height requiring clearance from within the Phytophthora infected area, must be mulched and retained on site.

The Contractor must wash down, or clean of soil, all equipment used.

The Contractor must undertake stump removal work in dry weather to minimise the spread of Phytophthora through water movement.

If mulched and cleared vegetative material cannot be contained within the infected area, the Contractor must dispose of it at a licensed waste depot. If offsite disposal is required, the Contractor must contain the material prior to transport, to prevent any potential to spread Phytophthora.

Materials

The Contractor must ensure materials brought onto the work site are free of Phytophthora.

The Contractor must store materials at the work site on a hard, dry, well-drained surface that does not drain towards vegetation, and is already clear of vegetation.

Water

The Contractor must ensure chlorinated mains water, sources free of Phytophthora, or water sterilised with an appropriate fungicide (i.e. Phytoclean®) or pool chlorine (60 mL to every 100 L of water) are used (refer Appendices 3 and 4).

Plant nursery stock

The Contractor must ensure plant nursery stock is Phytophthora-free prior to planting to ensure that Phytophthora is not introduced to Phytophthora-free or Phytophthora status-unknown sites. Nursery stock must be sourced from Nursery Industry Accreditation Scheme Australia (NIASA) accredited nurseries wherever practicable.

Hygiene breakdowns

The following measures must be implemented by the Contractor in the event of soil, plant material, wash-down effluent, or other potentially Phytophthora-infested material being deposited on a Phytophthora-free or Phytophthora status-unknown site:

- Demarcate a fenced buffer of 2 metres around the site of the breakdown.

- Move personnel, plant, equipment or vehicles out of the site only after wash-down.

- Sign-post the site “Phytophthora-Infested No Unauthorised Entry” or “Dieback Infested No Unauthorised Entry” and manage accordingly.

- Raise a non-conformance if appropriate.

- If the hygiene breakdown is a result of Contractor activities, the Contractor must (at the expense of the Contractor):

- treat the site as if it is contaminated until known otherwise.

- monitor the site annually for a period of three years (during which time there needs to be a wet spring or a wet summer season) for possible development of disease. If after two years there have been sufficient wet spring and/or wet summer seasons to allow Phytophthora symptoms to become evident, two years monitoring is sufficient. Monitoring must be undertaken towards the end of the active growing season (at the end of a wet spring or wet summer). Monitoring must be via visual inspection (including the use of photo points) and soil/plant tissue sampling (of dead or dying plants suspected of being infected with Phytophthora), with results confirmed via laboratory testing.

- undertake any soil/plant tissue sampling in accordance with laboratory requirements. The Contractor must obtain instructions from the laboratory on how to take a sample, the best time to take the sample, and how to store and transport it. Sampling usually involves digging up a dead or dying plant to get to the roots. Appropriate hygiene procedures are required during sampling activity.

- If an infestation is confirmed, the Contractor must:

- notify the SA Department of Environment, Water and Natural Resources (DEWNR) Ecologist Marine Interactions and Wildlife Biosecurity (Ms Renate Velzeboer), in order to update the Phytophthora database.

- prepare a management plan for the site upon confirmation of the infestation. The management plan must be prepared by a suitably qualified person (with a background in ecology or equivalent expertise) and endorsed by the Principal.

- If the hygiene breakdown is a result of DPTI activities, the above steps must be implemented by DPTI.

Kangaroo Island Phytophthora Risk Area

Phytophthora is known at a number of locations on Kangaroo Island. The above procedures apply to all areas identified in this Instruction, however the following additional specific procedures apply to Kangaroo Island. The Contractor must:

- before leaving the mainland for Kangaroo Island, clean (wash down) all mobile plant and machinery;

- avoid if practicable any works off the seal (particularly grading of unsealed shoulders, drain maintenance and sourcing of materials), particularly during the high-risk months of August to December;

- assess gravel pits as Phytophthora-free prior to use to ensure that Phytophthora is not introduced to Phytophthora-free or Phytophthora status-unknown areas (refer Section 7);

- use a power wash-down unit for cleaning mobile plant and equipment. There are two units available for hire from the District Council of Kangaroo Island (contact the Council’s Technical Program Manager or the depot). DPTI part funded one of these units, therefore DPTI is not required to pay a hire fee but may be required to contribute to the provision of chemicals; and

- before leaving Kangaroo Island for the mainland, clean (wash down) all mobile plant and machinery.

For any activities off the seal along the Playford Highway (in particular grading of unsealed shoulders and drain maintenance), the Contractor must commence from Kingscote proceeding towards Parndana using the following procedure:

- carry out activity such as grading in “bounds” of 3-4 km maximum length;

- clean plant (wash down) at the end of each “bound” before proceeding on; and

- clean down plant at the end of the last “bound” before returning to Kingscote.

## Medium Risk Sites

Medium Risk Sites may occur within the High or Moderate Potential Threat Areas of the State only.

Definition

- Site is within a Medium or High Potential Threat area;

AND

- Site occurs within or adjacent to remnant vegetation;

AND either of the following apply:

- known susceptible species have been identified in or adjacent to the site, and conducive soil types are present; or

- the site is located more than 5 km, but less than 10 km, from a confirmed infested site (irrespective of whether susceptible species have been identified in or adjacent to the site) (NatureMaps NatureMaps Home (environment.sa.gov.au

Pre-Works and On-Site Management Measures

The following procedures apply to any work site that has been designated as a Medium Risk Site.

Guidelines are given in Appendix 2 and Appendix 3 for the cleaning or wash-down of vehicles, equipment and footwear, where this has been identified in the following procedures.

Training

The Contractor must include relevant information and procedures to minimise the risk of spreading Phytophthora in the pre-works induction for all personnel working on the site.

In addition, the startup or toolbox meetings must include relevant information and procedures to minimise the risk of spreading Phytophthora.

Vehicle movement

The Contractor must contain movement of vehicles to formed areas wherever practicable, particularly in wet conditions.

The Contractor must ensure all plant is free of mud, soil and plant material (e.g. by dry brushing and/or clean with Phytoclean® or sodium hypochlorite (pool chlorine)) based on a visual inspection prior to:

- arriving at a site;

- moving to another Medium Risk site; and

- transporting gravel and other construction materials.

The Contractor must ensure plant is washed down prior to entering a Medium Risk Site.

The Contractor must ensure that work proceeds from un-infested (Phytophthora-free) or status unknown sites to known infested sites, wherever practicable.

Earthworks

Wherever practicable, the Contractor must:

- avoid leaving the road except under dry soil conditions;

- avoid using tracked vehicles as they are difficult to clean effectively;

- avoid grading beyond the areas previously graded (e.g. patrol grading); and

- conduct routine activities in “bounds” of several kilometres (e.g. 3-4 km), each interrupted by a clean-down to minimise the exposure risk of vegetation down-slope of the operation.

Drains

Wherever practicable, the Contractor must:

- clean out or repair drains in dry conditions only, unless during an emergency;

- avoid grading in watercourses or areas prone to flooding;

- ensure drains are constructed to avoid ponding of discharge water; and

- clean or wash down plant and equipment before moving away from a culvert or drain, if working outside formed areas.

Vegetation control

The Contractor must use vegetation control methods that do not disturb the soil, such as mowing, slashing, hand-pruning or herbicide application, in preference to grading.

Wherever practicable, the Contractor must carry out all works outside the formation in dry conditions only. The Contractor must avoid drains wherever practicable.

Materials

The Contractor must ensure materials brought onto the work site are free of Phytophthora.

The Contractor must store materials at the work site on a hard, dry, well-drained surface that does not drain towards vegetation, and is already clear of vegetation.

Plant nursery stock

The Contractor must ensure plant nursery stock is Phytophthora-free prior to planting to ensure that Phytophthora is not introduced to Phytophthora-free or Phytophthora status-unknown sites. Nursery stock must be sourced from Nursery Industry Accreditation Scheme Australia (NIASA) accredited nurseries wherever practicable.

## Low Risk Sites

Any site within the Low Potential Threat Area of the State is recognised as a Low Risk Site. Low Risk Sites however may also occur within High Potential and Medium Potential Threat Areas of the State (Figures 1 and 2).

Definition

- Site is within a Low Potential Threat area;

OR

- Site with no remnant native vegetation in or adjacent to the site;

OR

- Site that has non-conducive soil types;

OR

- Site that meets all of the following criteria:

- there is no infestation within 10 km of the site’

- it is not within a confirmed or suspected infested area; and

- there are no disease symptoms present;

OR

- sites within built-up areas.

Pre-Works and On-Site Management Measures

No Phytophthora control procedures are required.

# References

CPSM (2005) Management of Phytophthora cinnamomi for Biodiversity Conservation in Australia: Part 2. Risk Assessment Models for Species, Ecological Communities and Areas National Best Practice Guidelines. A report funded by the Commonwealth Government Department of the Environment and Heritage by the Centre for Phytophthora Science and Management, Murdoch University, Western Australia, accessed 22 March 2017, http://www.environment.gov.au/biodiversity/invasive/publications/p-cinnamomi.html

Department of the Environment and Heritage (2004). Phytophthora Root Rot. Australian Government.

Department for Environment and Heritage (2004). Phytophthora Root-rot fungus is killing our plants!, accessed online 22 March 2017,

Department of the Environment and Energy (2017). Phytophthora cinnamomi disease web page, accessed online 22 March 2017, http://www.environment.gov.au/biodiversity/invasive-species/diseases-fungi-and-parasites/phytophthora-cinnamomi-disease

Department of Planning, Transport and Infrastructure (2017). Part CH50 Environmental Protection Issues. Master Specification.

http://www.dpti.sa.gov.au/contractor_documents/specifications_-_division_CH

Kueh KH McKay SF, Facelli E, Facelli J, Velzeboer, RMA, Able AJ, Scott ES (2012) Response of selected South Australian native plant species to Phytophthora cinnamomi. Plant Pathology 61, 1165-78.

Nursery Industry Accreditation Scheme Australia (2005). NIASA Best Management Practice Guidelines. 3rd Edition.

Phytophthora Technical Group (2006). Phytophthora Management Guidelines. Government of South Australia. Second edition.

SA Department of Environment, Water and Natural Resources. Phytophthora Records accessed through NatureMaps http://www.naturemaps.sa.gov.au/

The Royal Botanic Garden Sydney, Phytophthora Dieback webpage, accessed online 22 March 2017, https://www.rbgsyd.nsw.gov.au/plants/pests-diseases/phytophthora-dieback

APPENDIX 1. 	DPTI roads within Phytophthora High Potential Threat Areas

Phytophthora High Potential Threat Areas of the State defined in Figure 2 include the following DPTI maintained roads:

Adelaide Hills and Fleurieu Peninsula

| RN 4384 | Barossa Valley Way | From MM 6.2 to 24.0 |
| --- | --- | --- |
| RN 4480 | Angaston – Birdwood | From MM 5.85 to 40.26 |
| RN 4483 | Lyndoch – Chain of Ponds | Entire Length of Road |
| RN 4486 | Williamstown – Birdwood | Entire Length of Road |
| RN 4489 | Tea Tree Gully – Mannum | From MM 0.0 to 56.30 |
| RN 4490 | Mount Torrens – Tungkillo | Entire Length of Road |
| RN 4492 | Chain of Ponds – Cudlee Creek | Entire Length of Road |
| RN 4495 | Birdwood – Verdun | Entire Length of Road |
| RN 4498 | Cudlee Creek – Verdun | Entire Length of Road |
| RN 4500 | South East Highway | From MM 0.0 to 41.14 |
| RN 4510 | Nairne Road | Entire Length of Road |
| RN 4515 | Aldgate – White Hill | From MM 0.0 to 29.0 |
| RN 4516 | Hahndorf – Echunga | Entire Length of Road |
| RN 4640 | Blackwood – Goolwa | From MM 0.0 to 65.54 |
| RN 4643 | Stirling – Strathalbyn | Entire Length of Road |
| RN 4646 | Mount Barker – Strathalbyn | Entire Length of Road |
| RN 4652 | Callington – Goolwa | Entire Length of Road |
| RN 4655 | Echunga - Meadows | Entire Length of Road |
| RN 4664 | Meadows – Willunga | Entire Length of Road |
| RN 4685 | Mount Compass – Goolwa | Entire Length of Road |
| RN 4688 | Victor Harbour – Goolwa | From MM 0.0 to 8.18 |
| RN 4760 | Noarlunga – Victor Harbor | Entire Length of Road |
| RN 4763 | Noarlunga – Cape Jervis | Entire Length of Road |
| RN 4787 | Willunga – Myponga | Entire Length of Road |
| RN 4790 | Myponga – Hindmarsh Valley | Entire Length of Road |
| RN 4793 | Yankalilla – Victor Harbor | Entire Length of Road |
| RN 5015 | Gawler – Kersbrook | Entire Length of Road |
| RN 5036 | Elizabeth – Williamstown | From MM 5.67 to 22.72 |
| RN 6000 | Gorge Road | Entire Length of Road |
| RN 6021 | Magill – Lobethal | Entire Length of Road |
| RN 6039 | Burnside – Balhannah | Entire Length of Road |
| RN 7380 | Mount Pleasant – Walker Flat | From MM 0.0 to 9.52 |
| RN 44809 | Balhannah – Little Hampton | Entire Length of Road |
| RN 44824 | Echunga – Mount Barker | Entire Length of Road |
| RN 47600 | Myponga Reservoir Access | Entire Length of Road |

Kangaroo Island

| RN 4880 | Playford Highway | MM 0.00 to 17.10 |
| --- | --- | --- |
| RN 4883 | Kingscote – Penneshaw | MM 0.00 to 53.14 |
| RN 4886 | Muston Hill – American River | MM 0.00 to 9.50 |

APPENDIX 2. 	Hygiene guidelines for vehicles

Cleaning vehicles and machinery is the single most important management action available apart from avoiding contact with Phytophthora.

Any equipment or vehicles that have been working in Phytophthora infected material must be cleaned down before travelling on Phytophthora-free surfaces.

Cleaning is a quarantine measure and therefore must be done properly every time and always carried out when specified in the Phytophthora control procedures for a project or operation. The value of the quarantine procedures can be destroyed by even a single failure.

Vehicles and machinery

Undertake a visual inspection to confirm that vehicles and machinery are free of soil, slurry (water and soil) or plant material.

Use vehicles that are easy to clean, such as machines with rubber tyres rather than tracks.

Undertake clean-down on a hard, well-drained site (e.g. road or compacted surface) away from native vegetation.

Situate the clean-down site just inside the infested zone to prevent the spread of Phytophthora to an uninfested area.

The clean-down site must be maintained in a clean state, and must be avoided by clean vehicles and machinery.

Clean down every piece of equipment, machinery and vehicle that has come into contact with soil or which could carry Phytophthora.

Phytophthora (dieback) boundaries within a work site must be signposted, for example:

or

Figure 1: Clean-down locations for entry to an infested work-site

Objects are likely to be Phytophthora-free when a visual inspection indicates the objects are free of:

- clods of soil and/or mud;

- slurry consisting of soil and water; and/or

- plant material, especially roots and lower stems.

The clean-down procedure for vehicles and machinery consists of two steps:

Step 1.	Dry brushing to remove mud and soil

(general hygiene measures for all sites)

- Try to remove mud and soil when it is dry.

- Remove all mud and soil with a hard brush or other tool, for example compressed air, brooms, shovels or steel rods.

- For vehicles and mobile plant pay particular attention to wheels, mudflaps and undercarriage.

- Disinfect the brush or tool used to remove mud and soil.

Step 2.	Disinfection to kill any Phytophthora that has not been removed

by dry brushing

(additional step for High Priority Sites)

- Do not wash down with water only – always use a disinfectant (e.g. Phytoclean®). The use of large amounts of water/disinfectant should be avoided – disinfection with a light spray is all that is required. Use clean (Phytophthora-free) water.

- Disinfect heavy equipment and vehicles using a pressurised spray unit (to minimise run-off) containing a disinfectant applied at label rates, for example:

- Phytoclean® (biodegradable and non-corrosive): Add 1 part to 50 parts water (2L /100L of water) or

- Sodium hypochlorite (pool chlorine): Add 1 part to 1500 parts water

- A supplier for Phytoclean® is Elders (Rural Supplier) at Virginia on (08) 8380 9324. Additional information can be found on http://www.phytoclean.com.au/.

- If using sodium hypochlorite, replenish after one day to maintain chemical effectiveness.

- Pay particular attention to earthmoving machinery, tracked vehicles and vehicles with protection plates where soil and roots may be trapped. Wheels, mudflaps, undercarriage and areas that are difficult to access must also be given particular attention.

- Allow the disinfectant to penetrate for at least one minute (preferably 10 minutes) before the vehicle or machinery leaves the clean-down area

- Ensure the tyres or tracks of vehicles are clean as they leave the clean-down area – do not drive through wash-down effluent.

- Do not allow mud and wash-down effluent to drain into native vegetation and surface waters, such as rivers, creeks, reservoirs and dams. If necessary, dig a trench to contain wash-down effluent.

- Where practicable, treat effluent by adding sodium hypochlorite, mixing it in thoroughly and leaving it to stand one day.

- Consider the disposal of the effluent as it may contain Phytophthora. For example, a drain could be constructed to collect and treat the effluent (see Figure 2 below). Drains could direct water to sediment infiltration sumps (which do not allow water to overflow).

- Drains must be made impermeable to water by compaction of suitable materials.

Figure 2: Example Phytophthora washdown facility

APPENDIX 3:	Phytophthora Hygiene Procedure for Minor Works and Site Inspections

Vehicles

When using vehicles within a Phytophthora zone, the Contractor must avoid any part of the vehicle coming into contact with the soil and remain on hard stand surfaces (i.e. a road) where practicable. If there is a need to park or move a vehicle through a Phytophthora zone where it will come into contact with soil, the Contractor must follow this procedure:

- When you leave the infection zone, move to an appropriate disinfection area, preferably a hard stand covered area free of soil.

- Remove any excessive soil build-up with a strong bristled brush.

- Spray all parts of the vehicle that came into contact with the soil with Phytoclean® using a spray bottle. Make sure you remove soil from all areas that came into contact with soil including mud flaps and the underside of the vehicle.

- Proceed to the uninfected area.

Footwear, small equipment and hand tools

The Contractor must disinfect footwear using a spray bottle or a footbath. The latter is useful when a large number of people need to disinfect their footwear at one location. The Contractor must follow this procedure:

- When you leave the infection zone, move to an appropriate disinfection area, preferably a hard stand covered area free of soil.

- Mud and soil must first be removed from footwear by brushing the sole of the shoe with a strong bristled brush.

- The disinfectant may be Phytoclean® (1 part to 10 parts water), Methylated spirits (70-100%) or household bleach (1 part to 4 parts water).

- Spray the sole of the shoes with disinfectant or if using a footbath step into the bath and move to a hard soil-free area.

- Step forward after disinfection to avoid recontamination of the shoes.

- Small equipment and hand tools must be cleaned by removing all soil and using a spray bottle containing the disinfectant.

- Disinfect the brush used to remove soil with Phytoclean®, Methylated spirits or household bleach on completion.

NB: The Contractor must not leave footbath unattended where children and animals may come in contact with the chemical

SUMMARY OF HYGIENE PROCEDURES*

|  | Hygiene Procedure | Disinfectant/rate | Comments |
| --- | --- | --- | --- |
| Small equipment, hand tools, footwear | Dry brushing Disinfection OR Dry brushing Footbath (useful for large groups of people) | Phytoclean® - 1 part to 10 parts water OR Household bleach - 1 part to 4 parts water OR Methylated spirits (70-100%) | All soil must be removed before disinfecting Avoid re-contaminating footwear Remember to disinfect brush or tool used in dry brushing |
| Vehicles | Dry brushing Spray all parts of the vehicle that came into contact with soil with a high pressure spray bottle | Phytoclean® - 1 part to 50 parts water OR Sodium hypochlorite (pool chlorine) 1 part to 1500 parts water | Avoid allowing vehicle to come in contact with soil wherever practicable Remember to use a high pressure spray bottle to remove soil, including spraying mud-flaps and the underside of the vehicle Remember to disinfect brush or tool used in dry brushing |

* Source: Phytophthora Technical Group (2006, 2nd edition), Phytophthora Management Guidelines, page 34,

APPENDIX 4.	Phytophthora Hygiene Kit

Personal Phytophthora Hygiene Kit

Examples of using the Phytophthora Hygiene Kit – Scrub and Disinfect

APPENDIX 5. 	Native plant species susceptible to Phytophthora

Native plant species susceptible to Phytophthora cinnamomi

in South Australia

The table below shows plant species that are known to be susceptible in South Australia (source: Phytophthora Management Guidelines, Phytophthora Technical Group 2006, 2nd Edition).

Symptoms of chlorosis, wilt, dieback and death have been observed AND Phytophthora cinnamomi has been isolated from the roots of plants of these species.

| Family | Species name | Common name |
| --- | --- | --- |
| Casuarinaceae | Allocasuarina verticillata | Drooping Sheoak |
| Dilleniaceae | Hibbertia spp. | Guinea-flower |
| Epacridaceae | Acrotriche halmaturina | Pink Ground-berry |
| Epacris impressa | Common Heath |
| Leucopogon virgatus | Common Bearded-Heath |
| Fabaceae | Pultenaea daphnoides | Large Leaved Bush-Pea |
| Pultenaea involucrata | Mount Lofty Bush-Pea |
| Pultenaea trifida | Kangaroo Island Bush-Pea |
| Mimosaceae | Acacia myrtifolia | Myrtle Wattle |
| Myrtaceae | Eucalyptus baxteri | Brown Stringybark |
| Eucalyptus obliqua | Messmate Stringybark |
| Leptospermum juniperinum | Prickly Tea-Tree |
| Proteaceae | Adenanthos macropodiana | Kangaroo Island Glandflower |
| Banksia marginata | Silver Banksia |
| Banksia ornata | Desert Banksia |
| Banksia serrata | Saw Banksia |
| Grevillea quinquenervis | Five-veined Grevillea |
| Grevillea rogersii | Rogers Grevillea |
| Isopogon ceratophyllus | Cone-bush |
| Petrophile multisecta | Kangaroo Island Conesticks |
| Tremandraceae | Tetratheca pilosa | Pink-eyed Susan |
| Xanthorrhoeaceae | Xanthorrhoea quadrangulata | Mount Lofty Grass-tree |
| Xanthorrhoea semiplana var. semiplan | Tufted Grass-tree |
| Xanthorrhoea semiplana var. tateana | Tate’s Grass-tree |

Plant species in BOLD are endemic to Kangaroo Island

Native Plant Species that may be susceptible to Phytophthora cinnamomi

in South Australia

The table below shows plant species that may be susceptible in South Australia (source: Phytophthora Management Guidelines, Phytophthora Technical Group 2006, 2nd Edition).

Symptoms of chlorosis, wilt, dieback and death have been observed and Phytophthora cinnamomi has been isolated from soil surrounding the roots of these species but NOT from the roots themselves.

| Family | Species | Common Name |
| --- | --- | --- |
| Compositae | Ixodia achillaeoides subsp. alata | Hills Daisy |
| Dilleniaceae | Hibbertia riparia | Erect Guinea-flower |
| Hibbertia sericea | Silky Guinea-flower |
| Epacridaceae | Acrotriche fasciculiflora | Pink Ground-berry |
| Leucopogon concurvus | Bearded Heath |
| Fabaceae | Daviesia brevifolia | Leafless Bitter-pea |
| Platylobium obtusangulum | Common Flat-pea |
| Mimosaceae | Acacia paradoxa | Kangaroo Thorn |
| Myrtaceae | Adenanthos terminalis | Adenanthos |
| Kunzea pomifera | Muntries |
| Proteaceae | Grevillea lavandulaceae | Lavender Grevillea |
| Rutaceae | Correa pulchella | Salmon Correa |
| Correa reflexa | Common Correa |

# Footnotes

1990 Bureau of Meteorology climate data

The NIASA is a national scheme run by the Nursery & Garden Industry for production nursery and growing media businesses, which operate in accordance with a set of national 'best practice' guidelines designed to minimise weeds and disease.

Ms Renate Velzeboer, Ecologist Marine Interactions and Wildlife Biosecurity

Department of Environment, Water and Natural Resources

Phone (08) 8552 0306	Mobile 0429 487 814	Email renate.velzeboer@sa.gov.au

# Text boxes

Superseded/repealed from 1 November 2021 – refer to https://www.dit.sa.gov.au/standards/environment

Phytophthora (Dieback) Control

Environmental Instruction 21.3

Medium risk

Low risk

Does the site occur within or adjacent to remnant vegetation?

Are there known susceptible species1 present or adjacent?

Low risk

Do any of the following apply?

- The site is infested

- There are disease symptoms present

- This is an infestation within 5km of the site

Is there an infestation within 5km of the site?

High risk

High risk

Does the site have conducive soil types?

Does the site have conducive soil2 types?

Is there an infestation within 10km of the site?

Low risk

Medium risk

Low risk

Is there an infestation within 10km of the site?

Low risk

Y

Y

Y

Y

Y

Y

Y

Y

N

N

N

N

N

N

N

N

Y

Y

Y

Y

Y

Y

Y

Y

N

N

N

N

N

N

N

N

DIEBACK FREE. NO ENTRY.

DIEBACK FREE. AUTHORISED ENTRY ONLY.

CLEAN-DOWN HERE.

HIGH RISK AREA

Work - Site

MODERATE

RISK

AREA

Disease

Status

Unknown

Uninfested

Cleandown location

Direction of movement

Infested