# LOCATING SEQUENTIAL STRINGS – Underground Services

| CODE | As Shown |
| --- | --- |
| DESCRIPTION | As Shown |
| MODEL | SERVICES * |
| TINNABLE | NO |
| DIRECTIONAL | NO |
| LOCATION INFORMATION | Located at natural surface with null level |
| COMMENTS | Text to be displayed in associated Services Model |

| Code | Service | Standard Text Display | Glossary of Classifications | Common Examples of Description |
| --- | --- | --- | --- | --- |
| DT | DPTI | ‘O/F’ (If relevant); ‘Description’; ‘D’; | O/F Optic Fibre | O/F D (SU) |
|  |  | Accuracy of capture (Refer Note Below) | P/L Public Lighting | T/S D (SU) |
|  |  |  | S/L Street Lighting | S/L D (SU) |
|  |  |  | T/S Traffic Signal |  |
| EL | ETSA | ‘O/F’ (If relevant); ‘HV’ or’LV’; ‘Voltage’ (If HV); ‘E’; | O/F Optic Fibre | HV 11kv E (SA) |
|  |  | Accuracy of capture (Refer Note Below) | HV High Voltage | HV E (SA) |
|  |  |  | LV Low Voltage | LV E (SA) |
|  |  |  | SL Street Lighting (Council Owned) | SL E (SA) |
|  |  |  |  | O/F E (SU) |
|  |  |  |  | DEAD E (SU) |

| Code | Service | Standard Text Display | Glossary of Classifications | Common Examples of Description |
| --- | --- | --- | --- | --- |
| GA | Gas | ‘Asset Owner’ (If not APA); ‘Diameter’; Classification; | GM –Gas Main | Envestra 100 mm SP HPGM G (SP) |
|  |  | ‘G’; Accuracy of capture (Refer Note Below) | HP – High Pressure | 300mm HP SP G (SU) |
|  |  |  | LP – Low Pressure | 40mm SP G (SU) |
|  |  |  | SP – Steel Pipe | 300mm HP SP G (SU) |
|  |  |  | CI – Cast Iron | MAIN G (SU) |
|  |  |  | POLY – Polycarbonate Tubing | 100mm CI G (SU) |
| RX | Rail | ‘O/F’ (If relevant); ‘HV’ or’LV’; ‘Voltage’ (If HV); ‘RX’; | HV High Voltage | HV 11kv RX (SA) |
|  |  | Accuracy of capture (Refer Note Below) | LV Low Voltage | LV RX (SA) |
| SE | Sewer | ‘Diameter’; Classification; ‘S’; Accuracy of capture (Refer Note Below) | PVCU Poly Vinly Chloride Unplasticised | 225mm CI S (SP) |
|  |  |  | CL Concrete Lined | 150mm PVCU S (SU) |
|  |  |  | CI Cast Iron | 400mm MSCL PUMP S (SU) |
|  |  |  | PE Poly Etheline |  |
|  |  |  | PUMP Pumping Main |  |
|  |  |  | GRAV Gravity Main |  |
|  |  |  | UNK Unknown |  |
| D* | Stormwater | ‘Diameter’; Classification; ‘SS’; Accuracy of capture (Refer Note Below) | RC Reinforced Concrete | 375mm RCP SS (SA) |
| C* |  |  | BC Box Culvert | 375*225mm RCBC SS (SU) |
|  |  |  | MS Mild Steel | 450mm RCP SS (SU) |
|  |  |  | CL Concrete Lined |  |
| TE | Telecommunications | ‘Asset Owner’; ‘O/F’ (If exists); ‘T’ Accuracy of capture (Refer Note Below) | O/F Optic Fibre | TELSTRA O/F T (SU) |
|  |  |  |  | OPTUS O/F T (SU) |
|  |  |  |  | DEAD T (SU) |
|  |  |  |  | OPTUS O/F NOT LOC (SU) |
|  |  |  |  | AMCOM O/F T (SU) |
| Code | Service | Standard Text Display | Glossary of Classifications | Common Examples of Description |
| WA | Water | ‘Diameter’; Classification; ‘W’: Accuracy of capture (Refer Note Below) | CL Concrete Lined | 375mm AC W (SP) |
|  |  |  | AC Asbestos Cement | 750mm MSCL W (SU) |
|  |  |  | MS Mild Steel | 375mm DICL W (SU) |
|  |  |  | CI Cast Iron | 150mm CICL W (SU) |
|  |  |  |  | 200mm UNKNOWN W (SU) |
| WR | Reclaimed Water | ‘Diameter’; Classification; ‘RW’; Accuracy of capture (Refer Note Below) | CL Concrete Lined | 375mm MS RW (SU) |
|  |  |  | MS Mild Steel |  |
| US | Unknown | ‘Diameter’; Classification; ‘U’; Accuracy of capture (Refer Note Below) |  | 150mm CICL U (SU) |

Note regarding accuracy of capture: At the completion of each line of text a letter for Services Active (SA), Direct (SD), Passive (SP) and Unverified (SU) shall be annotated.

Depthed Points

Where approximate depths have been located for services, show the approximate depth to the service from ground level such that the insertion point for the text is coincident with the Depthed point. For example, 1.2m shown with text rotated for clarity.